## Slide 1
UNIT 03 • LESSON 3 OF 4
Build & refine:
From sketch
to specimen
Workplanes, alignment, dimensions — building your alien in CAD.
Year 9 Design & Technologies • Double period (100 minutes)

## Slide 2
TODAY'S LESSON
COPY INTO WORKBOOK
What you'll learn and how you'll know
LEARNING OBJECTIVE
I can build my alien in CAD using precise dimensions, alignment and workplane techniques.
Why it matters
Today your sketch becomes a real 3D model. Every dimension, alignment and workplane choice you make here determines whether your alien actually prints.
SUCCESS CRITERIA
MUST
My alien is built in CAD with the body, head and at least one limb in place.
SHOULD
I have used Align and the workplane to position parts. All parts within 5–12.
COULD
I have refined a part after testing — the final version is better than the first attempt.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 2 • 2 / 15

## Slide 3
THE BIG PICTURE
Where this unit is heading
Over four double periods you'll learn to design, refine and print a 3D model. Today is Lesson 3: build & refine.
01
Intro to CAD
Navigate the workspace, place and edit primitive shapes, combine & cut.
02
Designing for print
Constraints of 3D printing: overhangs, supports, wall thickness, tolerances.
03
Build & refine
Workplanes, alignment, dimensions, troubleshooting. Develop against the brief.
TODAY
04
Export & print
Export STL, preview in slicer, peer feedback, submit.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 3 • 3 / 15

## Slide 4
TODAY'S RUN SHEET
How the 100 minutes flows
0–10
Hook & recap
Review L2 — what print constraints did you flag? Who fixed a risk in their sketch? Show your sketch.
10–30
Explicit teaching
Workplane, Align, Mirror, Duplicate. Live demo on the projector — follow on your screen.
30–75
You do — build
Work through the build log at your chosen tier. Teacher circulates; use the mid-build peer check.
75–85
Mid-build peer check
Swap screens. Partner checks part count, bounding box, at least one Hole. Fill in your workbook.
85–95
Iteration spotlight
Volunteers share before/after: one part that changed. Class discusses what improved and why.
95–100
Exit ticket
Three questions — CAD win, part count status, what to finish before L4. Stick slip in workbook.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 4 • 4 / 15

## Slide 5
EXPLICIT TEACHING & MODELLING
COPY INTO WORKBOOK
The workplane — stacking shapes at angles
DEFINITION
The workplane is the 'ground' your shapes sit on. Drag it onto any face to make that face the new base — this is how you attach shapes at angles and stack body parts.
1
Move the workplane
Drag the workplane (W key) from the corner onto any face of your model. The grid snaps to that face.
2
Place & build
Drag new shapes — they now sit on the face you chose. Great for angled limbs, fins, or tilted heads.
3
Reset when done
Press W and drag back to the default base. Always reset before saving or exporting your final file.
KEY TIPS
▸
Shortcut: press W to grab the workplane tool quickly.
▸
If shapes aren't sitting where expected — check your workplane hasn't been left on a face.
▸
You can workplane onto a hole's face too — useful for attaching things inside a cavity.
▸
Workplane confusion is the #1 source of floating shapes. Reset (W → drag to ground) before every export.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 5 • 5 / 15

## Slide 6
EXPLICIT TEACHING & MODELLING
COPY INTO WORKBOOK
Align — lining shapes up precisely
Select two or more shapes, then choose how to align them on each axis: left / centre / right (X) · front / centre / back (Y) · bottom / middle / top (Z).
X axis
Left · Centre · Right
Centres the head on the body. Lines up paired eyes or symmetrical wings.
Y axis
Front · Centre · Back
Pushes a beak or chin out to the front face. Aligns fins to the rear.
Z axis
Bottom · Middle · Top
Sits limbs flush on the body base. Stacks a head on top of a torso.
Tip · Hold Shift to multi-select before clicking Align. Align runs relative to the last-clicked shape.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 6 • 6 / 15

## Slide 7
EXPLICIT TEACHING & MODELLING
COPY INTO WORKBOOK
Mirror & Duplicate — work smarter
Mirror
What it does
Duplicate a shape and flip it across an axis to create a perfect mirror image.
How
Design one side (eye, arm, wing). Group the shapes. Then use Flip → Left/Right or Front/Back. Move into position.
Use it for
Symmetrical eyes, paired arms, matched fins. Design one, mirror the other — saves time and guarantees symmetry.
Shortcut: Flip buttons in toolbar
Duplicate
What it does
Ctrl+D copies a shape and remembers the last move. Press again to repeat that exact move.
How
Place a spike. Move it 12 mm to the right. Press Ctrl+D — a copy appears 12 mm further. Keep pressing for evenly spaced copies.
Use it for
Evenly spaced spikes, rings of eyes, identical legs. Set the gap once, duplicate the rest.
Shortcut: Ctrl+D (repeat: press again)
Align after
What it does
After mirroring or duplicating, use Align to lock the result into a precise position on the body.
How
Select the mirrored/duplicated part AND the body. Align on the axis you care about.
Use it for
Locks mirrored arms at the exact same height. Centres a row of spikes along the spine.
Shortcut: Align tool, multi-select with Shift
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 7 • 7 / 15

## Slide 8
MODELLING — WE DO
Live demo: positioning limbs (10 min)
Follow on your screen while I model on the projector. We'll use all three techniques on one alien body.
1
Set the workplane
Drag the workplane onto the left side of the torso. We'll attach one arm directly to the face.
2
Add & size the arm
Drag a cylinder. Resize to 8 × 8 × 25 mm. It should sit flush against the torso face.
3
Align the arm
Select arm + torso. Align: centre on Y (front/back). Middle on Z (height). Check it looks right.
4
Mirror the arm
Reset workplane. Select arm, Flip Left/Right. Move the copy to the right side. Align again.
5
Duplicate spikes
Add one cone (spike). Move it 15 mm along the spine. Press Ctrl+D three more times — four spikes, perfectly spaced.
6
Group & check
Select all. Group (Ctrl+G). Check bounding box in the inspector — should be under 80 × 80 × 80 mm.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 8 • 8 / 15

## Slide 9
APPLICATION OF LEARNING — YOU DO
COPY INTO WORKBOOK
Build log — tick each step as you go
Work through this in order. Your workbook has the full log — tick each box as you complete it in CAD.
Created the body
Main torso shape placed and sized on the workplane.
Added the head
Aligned centrally with the body using the Align tool.
Built one limb
Mirrored or duplicated for the other side.
Added eyes + Hole
At least one Hole used (mouth, eye socket, or nostril).
Added distinctive feature
The bold design choice from your specimen card.
Aligned the major axis
Used Align on at least one body axis.
Checked bounding box
Total dimensions ≤ 80 × 80 × 80 mm.
Grouped all parts
Everything combined into a single object.
Saved with clear name
e.g. YourName_Alien_v1 — ready for L4.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 9 • 9 / 15

## Slide 10
APPLICATION OF LEARNING — YOU DO
Build task: differentiated (45 min)
Choose the level that challenges you but is still finishable today. You can always level up.
FOUNDATION
Body + head + limbs
Build the torso, attach the head using Align, and add at least two limbs. Use the workplane to attach one limb at an angle. Include one Hole.
Success checks
Torso, head and two limbs in CAD.
Workplane used at least once.
One Hole included.
Part count between 5 and 12.
CORE
Full alien — all features
Complete alien built: body, head, limbs, eyes and distinctive feature. Mirror or Duplicate used for symmetrical parts. All dimensions match the master sketch.
Success checks
All five build log items ticked.
Mirror or Duplicate used.
Dimensions match sketch.
Bounding box ≤ 80 × 80 × 80 mm.
EXTENSION
Refine & iterate
Core done? Identify one part that could be improved. Make the change, record it in the iteration log (Version 1 vs Version 2). Prepare one print-risk fix.
Success checks
Iteration log completed.
At least one part redesigned.
Print risk identified and fixed.
File saved as v2 with clear name.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 10 • 10 / 15

## Slide 11
RESPONSIVE TEACHING — CHECK FOR UNDERSTANDING
Mid-build peer check
Swap screens with a partner. Answer the questions below for their design — record in your workbook.
WHAT TO CHECK
1
Part count
Count solids + holes. Is it between 5 and 12?
2
Bounding box
Fits inside 80 × 80 × 80 mm? Check the inspector panel.
3
At least one Hole
Mouth, eye socket, nostril — any Hole operation used?
4
Sits on the base
Does the model sit flat? Any floating parts?
5
Distinctive feature
Can you tell what the alien's 'one bold idea' is?
YOUR FEEDBACK TO PARTNER
★
Two things working well
Write in your workbook →
✎
One thing to refine
Write in your workbook →
?
One question for the designer
Write in your workbook →
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 11 • 11 / 15

## Slide 12
RESPONSIVE TEACHING
When it doesn't look right — troubleshoot it
Here are the most common problems at this stage.
Try the fix before asking for help.
Shape won't sit on the body
Why:
The workplane is probably set to the default ground — shapes land on the ground, not on the body face.
Fix:
Drag the workplane (W) onto the body face, then add the new shape. Reset when done.
Mirrored arm is in the wrong place
Why:
Flipping duplicates the shape, but doesn't move it — it lands on top of the original.
Fix:
After flipping, use the inspector to set an exact X position, or drag it across while watching the ruler.
Part count too high (> 12)
Why:
Each primitive — including each Hole — counts as one part.
Fix:
Delete parts that don't tell the viewer anything new. Ask: does this shape earn its place?
Model exceeds 80 mm bounding box
Why:
The torso or a limb is larger than intended — check the inspector, not visual estimation.
Fix:
Select the whole grouped model and read the dimensions. Scale down the part that's oversized.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 12 • 12 / 15

## Slide 13
RESPONSIVE TEACHING — CLASS DISCUSSION
Iteration spotlight — before & after
Three volunteers will share one part they changed. Class: watch for the design thinking behind each decision.
Specimen 1
VERSION 1 — what went wrong
(student describes)
VERSION 2 — what changed
(student describes)
Specimen 2
VERSION 1 — what went wrong
(student describes)
VERSION 2 — what changed
(student describes)
Specimen 3
VERSION 1 — what went wrong
(student describes)
VERSION 2 — what changed
(student describes)
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 13 • 13 / 15

## Slide 14
RESPONSIVE TEACHING
Exit ticket — last 5 minutes
1
CAD win
My biggest CAD achievement this lesson — what technique did I use and what did it do to my model?
2
Part count
My current part count is ___. If it's outside the 5–12 range, explain what I'll add or remove before Lesson 4.
✎
Next steps
What I need to finish before Lesson 4 — be specific (which part, what tool, what dimension).
Self-check tick boxes in your workbook · Stick the exit slip into page L3 when complete.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 3 • 14 • 14 / 15

## Slide 15
NEXT LESSON
Export & print
Specimen ready for transport — export STL, preview in slicer, peer feedback, submit.
Your alien — finished
All build log steps ticked. Grouped into one object. File saved with a clear name.
Your iteration log
At least one Version 1 / Version 2 comparison recorded in your workbook.
One print risk resolved
Know which part you were worried about — and confirm it now passes the 45° rule and wall check.
Lesson 4 of 4 • Unit: 3D Modelling with CAD