## Slide 1
UNIT 03 • LESSON 2 OF 4
Designing for print:
What the printer
can & can't do
Constraints, print rules, and designing your alien for real-world printing.
Year 9 Design & Technologies • Double period (100 minutes)

## Slide 2
COPY INTO WORKBOOK
TODAY'S LESSON
What you'll learn and how you'll know
LEARNING OBJECTIVE
I can identify 3D printing constraints and apply them to my alien design.
Why it matters
A model that looks great on screen can still fail at the printer. Understanding print constraints before you build saves you time, wasted plastic, and a very disappointing alien.
SUCCESS CRITERIA
MUST
Explain overhangs, wall thickness and tolerances in my own words.
SHOULD
Sketch my alien with labelled dimensions and a parts list within the 5–12 limit.
COULD
Start building in CAD and identify at least one printability risk in my design.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 2 • 2 / 14

## Slide 3
THE BIG PICTURE
Where this unit is heading
Over four double periods you'll learn to design, refine and print a 3D model. Today is Lesson 2: printing constraints.
01
Intro to CAD
Navigate the workspace, place and edit primitive shapes, combine & cut.
02
Designing for print
Overhangs, wall thickness, tolerances. Master sketch & specimen card.
TODAY
03
Build & refine
Workplanes, alignment, dimensions, troubleshooting. Develop against the brief.
04
Export & print
Export STL, preview in slicer, peer feedback, submit.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 3 • 3 / 14

## Slide 4
COPY INTO WORKBOOK
EXPLICIT TEACHING
Why some models fail at the printer
FDM printers build objects layer-by-layer from the bottom up. The printer can only place new plastic on top of something solid. That one rule creates three main problems.
1 Overhangs
Any surface leaning more than 45° from vertical has no support beneath it — the plastic droops or snaps off.
2 Thin walls
Walls under ~1.5 mm are too thin to be printed reliably and break easily once cool. They may not print at all.
3 Floating parts
Any shape that doesn't connect to the base or another shape will fall when gravity takes over. Every part needs to be anchored.
For this unit: no support material allowed. Your alien must stand on its own and pass the 45° rule.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 4 • 4 / 14

## Slide 5
COPY INTO WORKBOOK
EXPLICIT TEACHING & MODELLING
The 45° rule — overhangs
DEFINITION
An overhang is any part of your model that extends outward beyond the layer below it. FDM printers can handle overhangs up to about 45° — beyond that, the plastic sags.
OK — ≤45°
Each layer sits on the one below — printer is happy.
FAIL — >45°
New layers hang in mid-air — plastic sags or snaps.
HOW TO FIX IT
Rotate the part
Tilt limbs or spikes inward so they lean at ≤45° from the base.
Redesign the shape
Replace an outstretched arm with a bent one that curves down, not out.
Add a built-in support
Use a thin connecting strut (≥1.5 mm) to bridge between parts — design it as part of the creature.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 5 • 5 / 14

## Slide 6
COPY INTO WORKBOOK
EXPLICIT TEACHING & MODELLING
Wall thickness & tolerances
WALL THICKNESS
≥ 1.5 mm
Minimum wall for a solid, reliable print.
1.0 – 1.5 mm
Fragile — will probably print but may snap.
< 1.0 mm
Likely won't print at all.
Embossed text or raised details ≥ 1 mm. Engraved/cut details ≥ 0.5 mm.
TOLERANCE
Tolerance is the small gap you deliberately leave between parts that need to fit together or move independently.
Rule of thumb: leave 0.2 mm clearance between parts.
For your alien: tolerance matters if you design any joints, clip-together limbs, or attachable accessories.
PRINT RULES OF THUMB — COPY INTO WORKBOOK
▸ Min wall: 1.5 mm
▸ Overhang: ≤ 45°
▸ Bridge: < 5 mm span
▸ Tolerance: 0.2 mm
▸ First layer: wide and flat
▸ No support material
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 6 • 6 / 14

## Slide 7
RESPONSIVE TEACHING — CHECK FOR UNDERSTANDING
Spot the printability problems
Two alien designs are shown. With a partner: identify which parts will fail and why. Write your answers in your workbook.
SPECIMEN α
SPECIMEN β
What would YOU change to fix each specimen? Discuss, then note your answer in your workbook.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 7 • 7 / 14

## Slide 8
COPY INTO WORKBOOK
DESIGNING THE BRIEF
Lock in your alien — the specimen card
Before you sketch, decide the key facts. This locks in your concept so your dimensions are intentional, not random.
SPECIMEN CARD — FILL IN YOUR WORKBOOK
Designation (alien's name / species code)
Home environment (where does it live?)
Diet / energy source
Number of eyes
Number of limbs
Distinctive feature (the bold, memorable design choice)
Estimated part count
/ 12
Overall size (mm)
× × mm
Tip: your distinctive feature should be achievable with the basic shapes you already know — sphere, cylinder, cone, box, torus.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 8 • 8 / 14

## Slide 9
COPY INTO WORKBOOK
APPLICATION OF LEARNING — YOU DO
Master sketch — three views with dimensions
Draw your alien from the front, side and top. Label each part with its shape and dimensions in mm. Number every part — this becomes your parts list.
FRONT VIEW · grid = 5mm
SIDE VIEW · grid = 5mm
TOP VIEW · grid = 5mm
Parts list: number each part on your sketch, then list Part # → Shape → Body part → Dimensions (min 5, max 12 parts total)
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 9 • 9 / 14

## Slide 10
APPLICATION OF LEARNING — YOU DO
Design task: differentiated (40 min)
Choose the level that challenges you but is still finishable today. You can always level up.
FOUNDATION
Annotate & fix
Take one of the two specimen examples from the projector. Sketch it in your workbook, circle the problems, and draw a fixed version that passes the 45° rule and wall thickness checks.
Success checks
☐ At least two problems correctly identified.
☐ Fixed version has no overhangs >45°.
☐ Fixed version has walls ≥1.5 mm.
☐ Sketch is labelled with measurements.
CORE
Master sketch
Complete a three-view sketch of your alien (front, side, top) with mm dimensions on every part. Produce a parts list: part number, shape, body part, dimensions.
Success checks
☐ Three views drawn (front, side, top).
☐ Every part has a mm dimension.
☐ Part count is between 5 and 12.
☐ Specimen card is fully filled in.
EXTENSION
Start building in CAD
Sketch done? Open CAD. Build the torso and head of your alien. Flag any part you're worried might violate a print rule and note what you'll do about it.
Success checks
☐ Torso and head built in CAD.
☐ At least one Hole used.
☐ One print risk identified and a fix proposed.
☐ File saved with clear name for Lesson 3.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 10 • 10 / 14

## Slide 11
COPY INTO WORKBOOK
DESIGNING THE BRIEF
Part economy — earn every shape
BRIEF CONSTRAINTS — REMINDER
▸ Part count: 5–12 (solids + holes combined)
▸ Bounding box: fits inside 80 × 80 × 80 mm
▸ At least one Hole operation used
▸ Self-supporting — stands or sits alone
▸ No support material needed
▸ STL submitted by end of Lesson 4
▸ Original — not a copy of existing characters
PART ECONOMY
Every shape should earn its place.
Five clever parts beats fifteen messy ones.
Before you add another shape, ask:
Is this shape telling the viewer something new about my alien?
WHAT MAKES A GOOD ALIEN
1
Strange but believable
Give it a hint of biology.
2
Built from simple shapes
Show the parts working together.
3
One bold idea
Commit to a single distinctive choice.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 11 • 11 / 14

## Slide 12
TODAY'S RUN SHEET
How the 100 minutes flows
0–10
Hook & recap
Quick review of L1 — what's CAD, why do we group? Connect to today.
10–30
Explicit teaching
FDM printing, overhangs, wall thickness, tolerances. Spot the problems activity.
30–45
Specimen card
Students complete their alien's specimen card — lock in the concept.
45–80
You do — design
Master sketch at chosen tier. Teacher circulates, checks specs against brief.
80–90
Peer share
Swap sketches with a partner. Use the brief: does it meet the constraints?
90–95
Class discussion
What print risks did you spot in your own design? How will you fix them?
95–100
Exit ticket
Three questions — constraint, risk, fix. Stick the slip in your workbook.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 12 • 12 / 14

## Slide 13
RESPONSIVE TEACHING
Exit ticket — last 5 minutes
BEFORE YOU LEAVE
1
A print constraint I now understand — explain it in your own words.
2
A part of my alien I'm worried might not print — and why.
✎
What I'll change in my design to fix it — be specific.
Stick the slip into your workbook on page L2.
SELF-CHECK
Tick the boxes you've met:
☐ I can explain what an overhang is
☐ I understand the 45° rule
☐ I know the minimum wall thickness
☐ I understand tolerance
☐ I have a completed specimen card
☐ I have a master sketch with dimensions
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 2 • 13 • 13 / 14

## Slide 14
NEXT LESSON
Build & refine
From sketch to specimen — building your alien in CAD.
Bring your sketch
Master sketch with three views, labelled dimensions, and parts list.
Bring your specimen card
Completed with dimensions and part count confirmed in the brief range.
Bring a fix
Know how you'll solve any print risk you identified today — have a plan.
Lesson 3 of 4 • Unit: 3D Modelling with CAD