## Slide 1
UNIT 03 • LESSON 1 OF 4
From idea to object:
Intro to 3D Modelling with CAD
A four-lesson unit. By the end, you'll design and 3D-print your own alien.
Year 9 Design & Technologies • Double period (100 minutes)

## Slide 2
TODAY'S LESSON
What you'll learn and how you'll know
COPY INTO WORKBOOK
LEARNING OBJECTIVE
I can use CAD software to build a simple 3D model by combining and editing basic shapes.
Why it matters
Engineers, architects, surgeons, game designers and product makers all use CAD. By the end of this unit, you'll do what they do — model it, then print it.
SUCCESS CRITERIA
MUST
Open the CAD program, place a shape, and move/rotate/scale it correctly.
SHOULD
Combine at least two shapes using Group, and cut a hole using the Hole tool.
COULD
Use alignment and the workplane to position shapes precisely, and start sketching ideas for your alien.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 2 / 15

## Slide 3
THE BIG PICTURE
Where this unit is heading
Over four double periods you'll learn to design, refine and print a 3D model. Today is Lesson 1: the basics.
01
Intro to CAD
Navigate the workspace, place and edit primitive shapes, combine & cut. (Today)
TODAY
02
Designing for print
Constraints of 3D printing: overhangs, supports, wall thickness, tolerances. Begin model.
03
Build & refine
Workplanes, alignment, dimensions, troubleshooting. Develop the design against the brief.
04
Export & print
Export STL, preview in slicer, peer feedback, submit.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 3 / 15

## Slide 4
EXPLICIT TEACHING
What is CAD?
COPY INTO WORKBOOK
DEFINITION
CAD (Computer-Aided Design) is software used to create accurate 2D or 3D models of physical objects on a computer, before they are built or manufactured.
1
It's accurate
You can model to the exact millimetre. No more 'about that big.'
2
It's editable
Change a number — the whole model updates. No starting over.
3
It's shareable
Files can be sent to 3D printers, CNC machines or laser cutters.
WHERE YOU SEE CAD
Architecture
Buildings, bridges, fitouts.
Engineering
Cars, planes, machine parts.
Medicine
Prosthetics, dental crowns, implants.
Games & VFX
Characters, environments, props.
Everyday products
Your phone case, your shoes, the chair you're sitting on.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 4 / 15

## Slide 5
HOW IT FITS TOGETHER
From your screen to a real object
COPY INTO WORKBOOK
1
DESIGN
Build your model in CAD software (e.g. Tinkercad).
2
EXPORT
Save the model as an STL file — the standard for 3D printing.
3
SLICE
A slicer turns your STL into thin layers and sends them to the printer.
4
PRINT
The printer builds the object layer by layer, from the bottom up.
Key term: STL — a file format that describes the surface of a 3D model as a mesh of triangles.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 5 / 15

## Slide 6
MODELLING — THE TOOL
Meet your workspace
File Edit View Help
Shapes
Key parts of the workspace
A
Shapes panel
Drag primitives onto the workplane.
B
Workplane
The 'ground' your model sits on.
C
Selected object
Click to select; drag corners to resize.
D
Hole
A shape marked as 'Hole' removes material when grouped.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 6 / 15

## Slide 7
EXPLICIT TEACHING & MODELLING
The three core moves
COPY INTO WORKBOOK
MOVE
Reposition the object
How
Click & drag • Arrow keys (1mm) • Shift+Arrow (10mm)
Tip
Hold the black cone above the object to move it up in the Z axis (height).
ROTATE
Spin around an axis
How
Click the curved arrow handles • Snaps every 22.5° • Shift = no snap
Tip
Three axes: X (red), Y (green), Z (blue). Try rotating in each.
SCALE
Resize the object
How
Drag corner / edge handles • Type exact mm in the inspector • Shift = uniform
Tip
Lock proportions: drag a corner handle while holding Shift.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 7 / 15

## Slide 8
EXPLICIT TEACHING & MODELLING
Solids, holes & grouping
COPY INTO WORKBOOK
Every shape is either a Solid (it adds material) or a Hole (it removes material). They only combine when you Group them. Group again to nest, Ungroup to separate.
1. Solid + Hole
Two separate objects
2. Drag together
Overlapping — but still separate
3. Group (Ctrl+G)
Hole removed → one new shape
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 8 / 15

## Slide 9
MODELLING — WE DO
Walkthrough: build a name tile (10 min)
Follow along on your screen. I'll model it on the projector first, then you'll try.
1
Drag a Box onto the workplane.
Resize to 60 mm × 25 mm × 4 mm.
2
Drag the Text shape on top.
Type your first name. Move it up 1 mm.
3
Resize the text to fit.
Keep margins of ~3 mm on every side.
4
Add a Cylinder for a keyring hole.
Set it to Hole. Diameter 5 mm.
5
Position the cylinder near one end.
Make sure it goes all the way through.
6
Select all and Group (Ctrl+G).
Your name tile is now a single object.
Remember: all measurements in CAD use millimetres (mm). Watch the inspector panel to type exact sizes.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 9 / 15

## Slide 10
APPLICATION OF LEARNING — YOU DO
Practice task: differentiated (35 min)
Choose the level that pushes you a little — but is still finishable today. You can always level up.
FOUNDATION
Build a stamp tile
Make a 40×40×5 mm tile with a raised letter or symbol on top.
Success checks
Tile is exactly 40×40×5 mm.
Letter is raised by 2 mm.
Object is centred on the workplane.
All parts are grouped into one solid.
CORE
Design a keychain
A 60×25×4 mm keychain with your name and a 5 mm hole at one end.
Success checks
Text is legible and ≥ 4 mm tall.
Hole goes all the way through.
Hole is positioned safely (≥ 5 mm from any edge).
Final object is a single grouped solid.
EXTENSION
Alien head prototype
Skip the keychain. Start your unit project early — model an alien head only (3–6 parts).
Success checks
At least three primitive shapes used.
One Hole used (e.g. mouth or eye socket).
Uses Align or rotation to position parts.
Saved with a clear file name for next lesson.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 10 / 15

## Slide 11
LOOKING AHEAD — YOUR UNIT PROJECT
Brief: design an alien
COPY INTO WORKBOOK
THE BRIEF
Design and 3D-print an original alien — a creature that has never been seen before.
Your alien's body must be made by combining basic 3D shapes — keep your part count low so each shape is a deliberate choice.
CONSTRAINTS
Minimum 5 parts, maximum 12 parts (count solids + holes).
Fits inside an 80 × 80 × 80 mm bounding box.
Uses at least one Hole (a mouth, eye socket, nostril…).
Stands or sits on its own — no support material needed.
Submitted as an STL file by end of Lesson 4.
What makes a good alien?
1
Strange, but believable.
It should feel like it could survive somewhere — even if that somewhere is weird.
2
Built from simple shapes.
Cylinders for legs, spheres for eyes — show the parts working together.
3
One bold idea.
Three eyes? Stacked heads? Suction-cup feet? Commit to a choice.
Part economy: every shape should earn its place. Five clever parts beats fifteen messy ones.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 11 / 15

## Slide 12
DESIGNING THE BRIEF
Anatomy from primitives
COPY INTO WORKBOOK
Almost any creature you can imagine can be built from these basic shapes. Mix and match.
SPHERE
Heads, eyes, bellies
Squash or stretch for an egg-shape.
CYLINDER
Legs, arms, antennae
Tilt them to suggest movement.
CONE
Horns, claws, spikes
Group several for a fearsome look.
BOX
Torsos, jaws, teeth
Rotate 45° for a diamond shape.
TORUS
Collars, gills, rings
Doubles as a halo or jet exhaust.
HOLE
Mouths, eye sockets
Cut into solids to add detail without adding bulk.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 12 / 15

## Slide 13
TODAY'S RUN SHEET
How the 100 minutes flows
0–10
Hook & objective
What is CAD? Why does it matter? Today's success criteria.
10–25
Explicit teaching
Workspace tour, the three core moves, solids vs holes.
25–40
We do — name tile
Teacher-led walkthrough on the projector; students follow.
40–75
You do — practice
Independent task at your chosen tier. Teacher circulates.
75–85
Check-in & share
Show a partner. Compare against the success criteria.
85–95
Alien thinking
Sketch two alien ideas in your workbook. Label the shapes you'd use.
95–100
Exit ticket
Two stars and a wish — submit before you leave.
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 13 / 15

## Slide 14
RESPONSIVE TEACHING
Exit ticket — last 5 minutes
BEFORE YOU LEAVE
Two stars and a wish
★ One thing you can now do in CAD that you couldn't this morning.
★ One thing about your model you're proud of.
✎ One thing you still need help with — be specific.
Stick the slip into your workbook on page 1.
SELF-CHECK
Tick the boxes you've met:
I can place and edit shapes
I can move, rotate, scale precisely
I can combine shapes with Group
I can cut a Hole through a solid
I've sketched an alien idea
Year 9 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 1 • 14 / 15

## Slide 15
NEXT LESSON
Designing for the printer
Why some models print beautifully — and others fall over.
Bring a sketch
Two rough alien ideas, with dimensions in mm. Aim for 5–12 parts.
Bring questions
Anything from today you want me to walk through again.
Bring inspiration
A photo or drawing of a real creature you could remix into your alien.
Lesson 2 of 4 • Unit: 3D Modelling with CAD