## Slide 1
UNIT 03 • LESSON 4 OF 4
Export & print:
Specimen ready
for transport
STL export, slicer preview, peer feedback and final submission.
Year 7 Design & Technologies • Double period (100 minutes)

## Slide 2
TODAY'S LESSON
COPY INTO WORKBOOK
What you'll learn and how you'll know
LEARNING OBJECTIVE
I can export my alien as an STL file, check it in a slicer, and reflect on my design and making process.
Why it matters
Today is the day your alien becomes real. Every decision you made — every shape, every dimension — is about to be tested by a real printer. A clean export means your alien actually gets made.
SUCCESS CRITERIA
MUST
I can run every pre-flight check and export a valid STL file with the correct file name.
SHOULD
I have loaded my STL into the slicer and recorded the print time, filament use and any warnings.
COULD
I have completed my self-evaluation honestly and written a full unit reflection.
Year 7 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 4 • 2 • 2 / 15

## Slide 3
THE BIG PICTURE
Where this unit is heading
Over four double periods you'll learn to design, refine and print a 3D model. Today is Lesson 4: export & print.
01
Intro to CAD
Navigate the workspace, place and edit primitive shapes, combine & cut.
02
Designing for print
Constraints of 3D printing: overhangs, wall thickness, tolerances.
03
Build & refine
Workplanes, alignment, dimensions, troubleshooting. Develop against the brief.
04
Export & print
Export STL, preview in slicer, peer feedback, submit.
TODAY
Year 7 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 4 • 3 • 3 / 15

## Slide 4
TODAY'S RUN SHEET
How the 100 minutes flows
0–10
Hook & recap
Show your alien to the person next to you — one thing you're proud of, one thing you're still worried about. A few students share with the class.
10–30
Explicit teaching
What is an STL? How does the slicer work? Teacher demos the full export process step-by-step on the projector. Stop and ask if anything looks different on your screen.
30–70
You do — export & check
Work through the pre-flight checklist together, then export your STL and load it into the slicer. Your teacher will come around to help. Record your slicer notes in your workbook.
70–82
Final peer feedback
Show your alien to two classmates. Give each other one compliment and one helpful suggestion. Write it down in your workbook.
82–93
Self-eval & reflection
Circle your honest band on the self-evaluation sheet. Then answer the three reflection questions in your workbook — write in full sentences.
93–100
Submit & sign off
Check your STL is uploaded. Hand your workbook to your teacher with the exit ticket filled in. You're done!
Year 7 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 4 • 4 • 4 / 15

## Slide 5
EXPLICIT TEACHING & MODELLING
COPY INTO WORKBOOK
What is an STL file — and why does it matter?
DEFINITION
STL (Standard Triangle Language) describes a 3D model's surface as a mesh of triangles. It has no colour, no dimensions, no units — just shape. It is the universal language that slicers understand.
KEY TIPS
▸ Always export from a grouped model — ungrouped shapes create messy STLs.
▸ Save a numbered version before exporting (v1, v2, v3).
THE CAD → PRINT PIPELINE — STEP BY STEP
1
Design
Build your model in CAD software (e.g. Tinkercad).
2
Export
Save the model as an STL file — the triangulated surface.
TODAY
3
Slice
A slicer converts the STL into thin horizontal layers and sends them to the printer.
TODAY
4
Print
The printer builds the object layer-by-layer from the bottom up.
Key term: STL — the file format that describes the surface of a 3D model as a mesh of triangles.

## Slide 6
EXPLICIT TEACHING & MODELLING
COPY INTO WORKBOOK
How slicers read your model
Load your STL into the slicer and read these five numbers before you submit.
01
Print time
hours : minutes
Your estimated total print time. Times over 3 hours may mean the model is too complex or too large — check your bounding box.
02
Filament
grams used
How much plastic filament the print will use. Keeps track of material costs and print viability.
03
Layer height
mm per layer
Typically 0.2 mm. Lower = finer detail but slower. Your teacher will have set this — record what you see.
04
Support material
YES or NO
If the slicer shows YES, you have overhangs greater than 45°. Return to CAD and fix the offending part before submitting.
05
Warnings
count
Any red or orange warnings in the slicer preview. Record them all here. Zero warnings = you're ready.
Year 7 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 4 • 6 • 6 / 15

## Slide 7
MODELLING — WE DO
Live demo: export walkthrough (10 min)
Follow on your screen while I export on the projector. We'll go through every step — stop me if anything looks different on your screen.
1
Final group
Select everything on the canvas (Ctrl+A). Group (Ctrl+G). Confirm in the inspector: you should see one object, not many.
2
Reset workplane
Press W, drag the workplane back to the default grid. A rogue workplane can rotate your model in the slicer.
3
Check dimensions
Click your grouped object. Read the inspector: Width × Depth × Height. All three must be ≤ 80 mm.
4
Export → STL
In Tinkercad: top-right corner → Export → .STL under 'Include everything'. A file downloads automatically.
5
Name the file
Rename to: LastnameFirstname_Alien_v[n].stl e.g. SmithJordan_Alien_v3.stl — exact format, no spaces.
6
Upload & confirm
Drag the STL into the class submission folder. Tell your teacher. Do not close your Tinkercad file yet.
Year 7 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 4 • 7 • 7 / 15

## Slide 8
APPLICATION OF LEARNING — YOU DO
COPY INTO WORKBOOK
Pre-flight checklist — tick every item before you export
MANDATORY
All parts grouped into a single solid.
MANDATORY
Part count between 5 and 12 (inclusive).
MANDATORY
Bounding box ≤ 80 × 80 × 80 mm — confirmed in inspector.
MANDATORY
At least one Hole operation used and grouped.
MANDATORY
Model sits flat on the build plate — no floating parts.
EXPECTED
No overhangs greater than 45°.
EXPECTED
All walls ≥ 1.5 mm — no thin fins or spikes.
EXTENSION
Workplane reset to default before export.
MANDATORY
File named correctly: LastnameFirstname_Alien_v[n].stl
Year 7 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 4 • 8 • 8 / 15

## Slide 9
APPLICATION OF LEARNING — YOU DO
Export & check task: differentiated (40 min)
Work through the tier that fits where your model is right now. You can always level up.
FOUNDATION
Export & check
Work through the pre-flight checklist with your teacher's help. Group your model, export it as an STL and upload it to the class folder.
If your model isn't finished, get at least a body and head grouped and exported — that's okay.
Success checks
STL exported and uploaded to class folder.
File named correctly (check the format).
At least 5 parts and 1 Hole.
Started recording slicer notes.
CORE
Slicer preview + notes
Pre-flight check → export → load into the slicer → write down all five slicer readings in your workbook.
If you see warnings, try to fix them in CAD before submitting.
Success checks
All pre-flight checks ticked.
STL loaded into the slicer.
All five slicer readings recorded in workbook.
Zero warnings — or you know what each warning means.
EXTENSION
Fix, re-export & compare
If your slicer showed a warning, go back into CAD and fix it. Export again as v[n+1]. Compare your two slicer previews side by side.
Write in your workbook: what did you change and why?
Success checks
Slicer warning identified and understood.
Fix applied in CAD.
Re-exported with a new version number.
Before/after recorded in your workbook.
Year 7 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 4 • 9 • 9 / 15

## Slide 10
RESPONSIVE TEACHING
When it doesn't look right — troubleshoot it
Here are the most common problems at the export/slicer stage. Try the fix before asking for help.
Slicer shows the model in pieces
Why: You exported before grouping — the slicer sees multiple separate objects.
Fix
In Tinkercad, select all (Ctrl+A), group (Ctrl+G), then re-export. Check: inspector shows one object.
Model is rotated sideways in slicer
Why: The workplane was left on a model face when exported — the slicer treats the workplane as the floor.
Fix
Press W in Tinkercad, drag workplane back to the default grid, then re-export.
Slicer shows support material required
Why: At least one surface overhangs more than 45° — the slicer can't bridge it without scaffolding.
Fix
Rotate the model to find the overhang. Thicken a strut, lean the part inward, or add a built-in wedge underneath.
Print time is over 3 hours
Why: Model is likely larger than intended, or layer height is set very low. Large = slow; fine layers = slow.
Fix
Check bounding box — scale down if over 80 mm. Confirm your teacher's layer height setting (0.2 mm typical).
File name rejected on upload
Why: File name has spaces, wrong format, or wrong extension.
Fix
Rename to exactly: LastnameFirstname_Alien_v[n].stl — no spaces, no capitals on the extension.
Thin walls show as transparent in slicer
Why: A wall or spike is below 1.5 mm — the slicer renders it as too thin to print.
Fix
In CAD, select the part, increase thickness. Rule: no wall thinner than 1.5 mm.
Year 7 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 4 • 10 • 10 / 15

## Slide 11
RESPONSIVE TEACHING — CHECK FOR UNDERSTANDING
Final peer feedback
Show your slicer preview and your alien to two classmates. Record their feedback in your workbook.
WHAT TO SHOW YOUR PARTNER
1
Your alien in CAD — rotate it so they can see all sides.
2
Your slicer preview — the estimated time and any warnings.
3
Your workbook — the specimen card and master sketch.
Spend 5 minutes on each partner. You are giving feedback to two different people.
YOUR FEEDBACK TO PARTNER
★
Strongest design choice
Name one specific part or decision — not 'it looks cool'.
→ Write in your workbook
✎
One suggestion
One concrete, actionable thing they could improve.
→ Write in your workbook
?
One question for the designer
Something you genuinely want to know about their alien.
→ Write in your workbook
Year 7 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 4 • 11 • 11 / 15

## Slide 12
RESPONSIVE TEACHING
COPY INTO WORKBOOK
Self-evaluation — which band am I at?
Look at the rubric in your workbook. Circle the band you think you're at for each row. Be honest — there are no wrong answers here.
My design
Concept, sketches & shape choices
A
My alien is original with a clear idea behind it. Every shape was chosen on purpose. All three sketch views have measurements.
B
My alien has a clear look. Most shapes make sense. Two sketch views have measurements.
C
My alien looks okay. Some shapes feel random. One sketch view with some measurements.
D
My sketches are missing or have no measurements. The design doesn't match the brief.
My CAD skills
Tool use & how I built the model
A
I used Move, Rotate, Scale with exact mm numbers. I used Hole, Group and Align correctly. Everything is grouped into one solid.
B
I used all the main tools. A few things I moved by eye instead of typing exact numbers. Model is mostly correct.
C
I built the model but mostly dragged shapes around. The Hole tool might not be quite right.
D
I had trouble putting shapes together. The Hole tool isn't used or didn't work properly.
Print readiness
Does it meet the brief rules?
A
No overhangs over 45°. All walls ≥1.5 mm. 5–12 parts. Fits the 80 mm box. Slicer shows zero warnings.
B
Mostly print-ready. Very small overhangs or slightly thin walls — nothing major. STL submitted on time.
C
The slicer shows some warnings — thin walls or steep overhangs. STL submitted.
D
Several rules broken — part count, size or overhangs. STL not submitted or won't open.
Year 7 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 4 • 12 • 12 / 15

## Slide 13
RESPONSIVE TEACHING — CLASS DISCUSSION
COPY INTO WORKBOOK
Unit reflection — what did I actually learn?
Three volunteers will share a reflection. Class: listen to what surprised people or what they'd do differently.
01
The most useful thing I learnt in this unit
Hint: Not just a tool name — what can you actually DO now that you couldn't before? What would you use it for?
(student shares)
02
Something that didn't go to plan — and what I did about it
Hint: It's okay if something went wrong. What was the problem? Did you fix it, work around it, or change your design?
(student shares)
03
If I built this alien again from scratch, I would…
Hint: Name one specific thing — a shape, a measurement, a decision. What would you do differently and why?
(student shares)
Year 7 Design & Technologies • Unit: 3D Modelling with CAD
Lesson 4 • 13 • 13 / 15

## Slide 14
RESPONSIVE TEACHING
Exit ticket — last 5 minutes
α
Specimen sign-off
My specimen's name and final part count. STL file name I submitted:
Write below the line —
β
Slicer one-liner
Estimated print time ___ h ___ min. Filament ___ g. Support material: YES / NO. Warnings:
Write below the line —
γ
One sentence
Describe this creature to someone who has never seen it — one sentence only:
Write below the line —
Self-check tick boxes in your workbook · Hand this exit slip to your teacher when complete.

## Slide 15
END OF TRANSMISSION
Mission
Complete
Your alien — being printed
Your STL is uploaded and in the print queue. The creature you designed and built is on its way to becoming a real object you can hold.
Your workbook — complete
Pre-flight checks, slicer notes, peer feedback, self-evaluation and reflection all done. This is the evidence of your design process.
What you can do now
You can take an idea in your head, design it in CAD, check it for print rules, and turn it into a real 3D-printed object. That's a big deal.
Xeno-Lab · Unit 03 · 3D Modelling with CAD